## Slide 1: OSCI TLM-2.0
The Transaction Level Modeling standard of the Open SystemC Initiative (OSCI)

## Slide 2: OSCI TLM-2.0
Software version: TLM-2.0
Document version: ja6
This presentation authored by: John Aynsley, Doulos
Copyright © 2007-2008 by Open SystemC Initiative. All rights reserved

## Slide 3: CONTENTS
Introduction
Transport Interfaces
DMI and Debug Interfaces
Sockets
The Generic Payload
The Base Protocol
Analysis Ports
<number>

## Slide 4: INTRODUCTION
Transaction Level Modeling 101
OSCI TLM-1 and TLM-2
Coding Styles
Structure of the TLM-2.0 Kit
<number>

## Slide 5: Transaction Level Modeling 101
<number>
RTL
Simulate every event
RTL
Functional Model
Functional Model
100-10,000 X faster simulation
write(address,data)
Pin accurate, cycle accurate
Transaction level - function call

## Slide 6: Reasons for Using TLM
<number>
Software development
Firmware / software
Accelerates product release schedule
Test bench
Hardware verification
RTL
TLM = golden model
Architectural modeling
TLM
Fast enough
Ready before RTL

## Slide 7: Typical Use Cases for TLM
Represents key architectural components of hardware platform
Architectural exploration, performance modeling
Software execution on virtual model of hardware platform
Golden model for hardware functional verification
Available before RTL
Simulates much faster than RTL
<number>

## Slide 8: OSCI TLM Development
<number>

## Slide 9: TLM-1.0  TLM-2.0
TLM-2.0 is the new standard for interoperability between memory mapped bus models
  Incompatible with TLM-2.0-draft1 and TLM-2.0-draft2
TLM-1.0 is not deprecated (put, get, nb_put, nb_get, transport)
TLM-1.0 is included within TLM-2.0
  Migration path from TLM-1.0 to TLM-2.0 (see examples)
<number>

## Slide 10: TLM-2 Requirements
Transaction-level memory-mapped bus modeling
Register accurate, functionally complete
Fast enough to boot software O/S in seconds
Loosely-timed and approximately-timed modeling
Interoperable API for memory-mapped bus modeling
Generic payload and extension mechanism
Avoid adapters where possible
<number>
See TLM_2_0_requirements.pdf

## Slide 11: Use Cases, Coding Styles and Mechanisms
<number>
Blocking interface
Non-blocking interface
DMI
Sockets
Quantum
Generic payload
Mechanisms
Use cases
Software development
Architectural analysis
Hardware verification
Software performance
Loosely-timed
Approximately-timed
TLM-2 Coding styles
Phases

## Slide 12: Coding Styles
Loosely-timed
  Only sufficient timing detail to boot O/S and run multi-core systems
  Processes can run ahead of simulation time (temporal decoupling)
  Each transaction has 2 timing points: begin and end
  Uses direct memory interface (DMI)
Approximately-timed
  aka cycle-approximate or cycle-count-accurate
  Sufficient for architectural exploration
  Processes run in lock-step with simulation time
  Each transaction has 4 timing points (extensible)
Guidelines only – not definitive
<number>

## Slide 13: Loosely-timed
<number>
Process 1
Process 2
Process 3
Quantum
Quantum
Quantum
Quantum
sc_time_stamp() advances in multiples of the quantum
Each process runs ahead up to quantum boundary
Deterministic communication requires explicit synchronization

## Slide 14: Approximately-timed
<number>
Process 1
Process 2
Process 3
0
10
20
30
40
50
Annotated delays
Each process is synchronized with SystemC scheduler
Delays can be accurate or approximate

## Slide 15: The TLM 2.0 Classes
Interoperability layer for bus modeling
<number>
IEEE 1666™ SystemC
TLM-1 standard
TLM-2 core interfaces:
Blocking transport interface
Non-blocking transport interface
Direct memory interface
Debug transport interface
Analysis interface
Initiator and target sockets
Analysis ports
Generic payload
Phases
Utilities:
Convenience sockets
Payload event queues
Quantum keeper
Instance-specific extn

## Slide 16: Interoperability Layer
<number>
Target
Initiator
1. Core interfaces and sockets
2. Generic payload
Command
Address
Data
Byte enables
Response status
Extensions
3. Base protocol
BEGIN_REQ
END_REQ
BEGIN_RESP
END_RESP
Maximal interoperability for memory-mapped bus models

## Slide 17: Utilities
<number>
tlm_utils
  Convenience sockets
  Payload event queues
  Quantum keeper
  Instance-specific extensions
Productivity
Shortened learning curve
Consistent coding style
Not part of the interoperability layer – write your own?

## Slide 18: Directory Structure
<number>
include/tlm
  tlm_h
    tlm_req_rsp
    tlm_trans
      tlm_2_interfaces
      tlm_generic_payload
      tlm_sockets
    tlm_quantum
    tlm_analysis
  tlm_utils
docs
  doxygen
examples
unit_test
TLM-1.0 legacy
TLM-2 interoperability classes
TLM-2 core interfaces
TLM-2 generic payload
TLM-2 initiator and target sockets
TLM-2 global quantum
TLM-2 analysis interface, port, fifo
TLM-2 utilities

## Slide 19: TRANSPORT INTERFACES
Initiators and Targets
Blocking Transport Interface
Timing Annotation and the Quantum Keeper
Non-blocking Transport Interface
Timing Annotation and the Payload Event Queue
<number>

## Slide 20: Initiators and Targets
<number>
Initiator
Interconnect component
0, 1 or many
Target
Initiator socket
Target socket
Initiator socket
Target socket
Forward path
Backward path
Forward path
Backward path
Transaction object
References to a single transaction object are passed along the forward and backward paths
Notes: <number>

## Slide 21: TLM-2 Connectivity
Target/ Initiator
Target/ Initiator
Initiator
Target
Target
<number>
Initiator
Interconnect
Target
Interconnect
Initiator
Transaction memory management needed
Notes: <number>

## Slide 22: Convergent Paths
<number>
Target
Interconnect
Initiator
Initiator
Notes: <number>

## Slide 23: Blocking versus Non-blocking Transport
Blocking transport interface
  Includes timing annotation
  Typically used with loosely-timed coding style
  Forward path only
Non-blocking transport interface
  Includes timing annotation and transaction phases
  Typically used with approximately-timed coding style
  Called on forward and backward paths
Share the same transaction type for interoperability
Unified interface and sockets – can be mixed
<number>

## Slide 24: TLM-2 Core Interfaces - Transport
<number>
void b_transport( TRANS& , sc_time& ) ;
tlm_sync_enum nb_transport_fw( TRANS& , PHASE& , sc_time& );
tlm_fw_nonblocking_transport_if
tlm_blocking_transport_if
tlm_sync_enum nb_transport_bw( TRANS& , PHASE& , sc_time& );
tlm_bw_nonblocking_transport_if

## Slide 25: TLM-2 Core Interfaces - DMI and Debug
<number>
void invalidate_direct_mem_ptr( sc_dt::uint64 start_range,
sc_dt::uint64 end_range ) ;
unsigned int transport_dbg( TRANS& trans ) ;
tlm_fw_direct_mem_if
bool get_direct_mem_ptr( TRANS& trans , tlm_dmi& dmi_data ) ;
tlm_bw_direct_mem_if
tlm_transport_dbg_if
May all use the generic payload transaction type

## Slide 26: Blocking Transport
<number>
template < typename TRANS = tlm_generic_payload >
class tlm_blocking_transport_if : public virtual sc_core::sc_interface {
public:
  virtual void b_transport ( TRANS& trans , sc_core::sc_time& t ) = 0;
};
Timing annotation
Transaction object
Transaction type

## Slide 27: Blocking Transport
<number>
Initiator
Target
b_transport(t, 0ns)
Call
Simulation time = 100ns
Simulation time = 140ns
wait(40ns)
Initiator is blocked until return from b_transport
Return
b_transport(t, 0ns)
b_transport(t, 0ns)
Call
Return
b_transport(t, 0ns)

## Slide 28: Timing Annotation
<number>
virtual void b_transport ( TRANS& trans , sc_core::sc_time& delay )
{
// Behave as if transaction received at sc_time_stamp() + delay
...
delay = delay + latency;
}
Recipient may
  Execute transactions immediately, out-of-order – Loosely-timed
  Schedule transactions to execution at proper time – Approx-timed
  Pass on the transaction with timing annotation
b_transport( transaction, delay );
// Behave as if transaction received at sc_time_stamp() + delay

## Slide 29: Temporal Decoupling
<number>
Initiator
Target
b_transport(t, 0ns)
Call
Simulation time = 100ns
Simulation time = 140ns
wait(40ns)
Local time offset
Return
b_transport(t, 5ns)
+5ns
b_transport(t, 20ns)
Call
+20ns
Return
b_transport(t, 25ns)
+25ns
b_transport(t, 30ns)
Call
+30ns
Return
b_transport(t, 5ns)
+5ns

## Slide 30: The Time Quantum
<number>
Initiator
Target
b_transport(t, 950ns)
Call
Simulation time = 1us
Simulation time = 2us
wait(1us)
Local time offset
Return
b_transport(t, 970ns)
+970ns
b_transport(t, 990ns)
Call
+990ns
Return
b_transport(t, 1010ns)
+1010ns
+950ns
Quantum = 1us
b_transport(t, 0ns)
Call
+0ns

## Slide 31: The Quantum Keeper (tlm_quantumkeeper)
Quantum is user-configurable
Processes can check local time against quantum
SMALL
quantum
lever
BIG
speed
debug

## Slide 32: Quantum Keeper Example
<number>
struct Initiator: sc_module
{
tlm_utils::simple_initiator_socket<Initiator> init_socket;
tlm_utils::tlm_quantumkeeper m_qk;
SC_CTOR(Initiator) : init_socket("init_socket") {
...
m_qk.set_global_quantum( sc_time(1, SC_US) );
m_qk.reset();
}
void thread() { ...
for (int i = 0; i < RUN_LENGTH; i += 4) {
...
delay = m_qk.get_local_time() ;
init_socket->b_transport( trans, delay );
m_qk.set( delay );
m_qk.inc( sc_time(100, SC_NS) );
if ( m_qk.need_sync() )
m_qk.sync();
}
}
};
The quantum keeper
Replace the global quantum
Recalculate the local quantum
Time consumed by transport
Check local time against quantum
and sync if necessary
Further time consumed by initiator

## Slide 33: Non-blocking Transport
<number>
enum tlm_sync_enum { TLM_ACCEPTED, TLM_UPDATED, TLM_COMPLETED };
template < typename TRANS = tlm_generic_payload,
typename PHASE = tlm_phase>
class tlm_fw_nonblocking_transport_if : public virtual sc_core::sc_interface {
public:
virtual tlm_sync_enum nb_transport( TRANS& trans,
PHASE& phase,
sc_core::sc_time& t ) = 0;
};
Trans, phase and time arguments set by caller and modified by callee

## Slide 34: tlm_sync_enum
TLM_ACCEPTED
  Transaction, phase and timing arguments unmodified (ignored) on return
  Target may respond later (depending on protocol)
TLM_UPDATED
  Transaction, phase and timing arguments updated (used) on return
  Target has advanced the protocol state machine to the next state
TLM_COMPLETED
  Transaction, phase and timing arguments updated (used) on return
  Target has advanced the protocol state machine straight to the final phase
<number>

## Slide 35: Notation for Message Sequence Charts
<number>
-, BEGIN_REQ, 0ns
status = nb_transport ( trans, phase, delay ) ;
Call
Local time
Simulation time = 5us
+10ns
+20ns
For temporal decoupling, local time is added to simulation time (explained on slides)
= sc_time_stamp()
TLM_COMPLETED, BEGIN_RESP, 10ns
Return
Arguments passed to function
Values returned from function

## Slide 36: Using the Backward Path
<number>
Initiator
Target
Phase
TLM_ACCEPTED, -, -
Return
BEGIN_REQ
-, BEGIN_REQ, 0ns
Call
TLM_ACCEPTED, -, -
Return
Simulation time = 100ns
-, END_REQ, 0ns
END_REQ
Call
Simulation time = 110ns
TLM_ACCEPTED, -, -
Return
-, BEGIN_RESP, 0ns
BEGIN_RESP
Call
Simulation time = 120ns
TLM_COMPLETED, -, -
Return
END_RESP
-, END_RESP, 0ns
Call
Simulation time = 130ns
Transaction accepted now, caller asked to wait

## Slide 37: Using the Return Path
<number>
Initiator
Target
Phase
BEGIN_REQ
-, BEGIN_REQ, 0ns
Call
Simulation time = 100ns
TLM_COMPLETED, END_RESP, 5ns
Return
-, BEGIN_RESP, 0ns
BEGIN_RESP
Call
Simulation time = 150ns
TLM_UPDATED, END_REQ, 10ns
Return
END_REQ
Simulation time = 110ns
Callee annotates delay to next transition, caller waits
END_RESP
Simulation time = 155ns

## Slide 38: Early Completion
<number>
Initiator
Target
Phase
BEGIN_REQ
-, BEGIN_REQ, 0ns
Call
TLM_COMPLETED, -, 10ns
Return
END_RESP
Simulation time = 110ns
Callee annotates delay to next transition, caller waits
Simulation time = 100ns

## Slide 39: Timing Annotation
<number>
Initiator
Target
Phase
-, BEGIN_REQ, 10ns
Call
TLM_ACCEPTED, -, -
Return
Simulation time = 100ns
Payload Event Queue
Simulation time = 110ns
BEGIN_REQ
-, END_REQ, 10ns
Call
Simulation time = 125ns
TLM_ACCEPTED, -, -
Return
Payload Event Queue
END_REQ
Simulation time = 135ns

## Slide 40: Payload Event Queue
<number>
template <class PAYLOAD>
class peq_with_get : public sc_core::sc_object
{
public:
peq_with_get( const char* name );
void notify( PAYLOAD& trans, sc_core::sc_time& t );
void notify( PAYLOAD& trans );
transaction_type* get_next_transaction();
sc_core::sc_event& get_event();
}
while (true) {
wait( m_peq.get_event() );
while ( (trans = m_peq.get_next_transaction()) != 0) {
...

## Slide 41: DMI AND DEBUG INTERFACES
Direct Memory Interface
Debug Transport Interface
<number>

## Slide 42: DMI and Debug Transport
<number>
Direct Memory Interface
  Gives an initiator a direct pointer to memory in a target, e.g an ISS
  By-passes the sockets and transport calls
  Read or write access by default
  Extensions may permit other kinds of access, e.g. security mode
  Target responsible for invalidating pointer
Debug Transport Interface
  Gives an initiator debug access to memory in a target
  Delay-free
  Side-effect-free
May share transactions with transport interface

## Slide 43: Direct Memory Interface
<number>
Initiator
Interconnect component
Target
Forward path
Backward path
Forward path
Backward path
Interconnect may modify address and invalidated range
Transport, DMI and debug may all use the generic payload
invalidate_direct_mem_ptr( start_range, end_range );
tlm_bw_direct_mem_if
tlm_fw_direct_mem_if
status = get_direct_mem_ptr( transaction, dmi_data );
Access requested
Access granted

## Slide 44: DMI Transaction and DMI Data
<number>
Requests read or write access
For a given address
Permits extensions
class tlm_dmi
DMI Transaction
unsigned char* dmi_ptr
uint64 dmi_start_address
uint64 dmi_end_address
dmi_type_e dmi_type;
sc_time read_latency
sc_time write_latency
Direct memory pointer
Region granted for given access type
Latencies to be observed by initiator
Read, write or read/write

## Slide 45: DMI Rules 1
Initiator requests DMI from target at a given address
DMI granted for a particular access type and a particular region
  Target can only grant a single contiguous memory region containing given address
  Target may grant an expanded memory region
  Target may promote READ or WRITE request to READ_WRITE
Initiator may assume DMI pointer is valid until invalidated by target
Initiator may keep a table of DMI pointers
<number>

## Slide 46: DMI Rules 2
DMI request and invalidation use same routing as regular transactions
The invalidated address range may get expanded by the interconnect
Target may grant DMI to multiple initiators (given multiple requests)
  and a single invalidate may knock out multiple pointers in multiple initiators
Use the Generic Payload DMI hint (described later)
Only makes sense with loosely-timed models
<number>

## Slide 47: Debug Transport Interface
<number>
Initiator
Interconnect component
Target
Forward path
Backward path
Forward path
Backward path
Interconnect may modify address, target reads or writes data
Uses forward path only
tlm_transport_dbg_if
num_bytes = transport_dbg( transaction );
Command
Address
Data pointer
Data length
Extensions

## Slide 48: SOCKETS
Initiator and target sockets
Simple sockets
Tagged sockets
Multi-port sockets
<number>

## Slide 49: Initiator and Target Sockets
<number>
Initiator
Target
Target socket
nb_transport_bw()
invalidate_direct_mem_ptr()
Initiator socket
b_transport ()
nb_transport_fw()
get_direct_mem_ptr()
transport_dbg()
Sockets provide fw and bw paths and group interfaces

## Slide 50: Benefit of Sockets
Group the transport, DMI and debug transport interfaces
Bind forward and backward paths with a single call
Strong connection checking
Have a bus width parameter
Using core interfaces without sockets is not recommended
<number>

## Slide 51: Sockets and Transaction Types
All interfaces templated on transaction type
Use the generic payload and base protocol for interoperability
  Use with transport, DMI and debug transport
  Supports extensions
  Even supports extended commands and phases
  Ignorable extensions allow interoperability
  Mechanism to disallow socket binding for non-ignorable extensions
  Described later
<number>

## Slide 52: Standard Socket Classes
<number>
template < unsigned int BUSWIDTH = 32,
typename TYPES = tlm_base_protocol_types,
int N = 1,
sc_core::sc_port_policy POL = sc_core::SC_ONE_OR_MORE_BOUND>
class tlm_initiator_socket
...
class tlm_target_socket
Part of the interoperability layer
Initiator socket must be bound to an object that implements entire backward interface
Target socket must be bound to an object that implements entire forward interface
Can mix blocking and non-blocking calls – target must support both together
Allow hierarchical binding

## Slide 53: Socket Binding Example 1
<number>
struct Initiator: sc_module, tlm::tlm_bw_transport_if<>
{
tlm::tlm_initiator_socket<> init_socket;
SC_CTOR(Initiator) : init_socket("init_socket") {
SC_THREAD(thread);
init_socket.bind( *this );
}
void thread() { ...
init_socket->b_transport( trans, delay );
init_socket->nb_transport_fw( trans, phase, delay );
init_socket->get_direct_mem_ptr( trans, dmi_data );
init_socket->transport_dbg( trans );
}
virtual tlm::tlm_sync_enum nb_transport_bw( ... ) { ... }
virtual void invalidate_direct_mem_ptr( ... ) { ... }
};
Protocol type defaults to base protocol
Initiator socket bound to initiator itself
Calls on forward path
Methods for backward path
Combined interface required by socket

## Slide 54: Socket Binding Example 2
<number>
struct Target: sc_module, tlm::tlm_fw_transport_if<>
{
tlm::tlm_target_socket<> targ_socket;
SC_CTOR(Target) : targ_socket("targ_socket") {
targ_socket.bind( *this );
}
virual void b_transport( ... ) { ... }
virtual tlm::tlm_sync_enum nb_transport_fw( ... ) { ... }
virtual bool get_direct_mem_ptr( ... ) { ... }
virtual unsigned int transport_dbg( ... ) { ... }
};
SC_MODULE(Top) {
Initiator *init;
Target *targ;
SC_CTOR(Top) {
init = new Initiator("init");
targ = new Target("targ");
init->init_socket.bind( targ->targ_socket );
}
};
Protocol type default to base protocol
Target socket bound to target itself
Methods for forward path
Bind initiator socket to target socket
Combined interface required by socket

## Slide 55: Convenience Sockets
<number>
The “simple” sockets
  simple_initiator_socket and simple_target_socket
    In namespace tlm_utils
    Derived from tlm_initiator_socket and tlm_target_socket
  “simple” because they are simple to use
    Do not bind sockets to objects (implementations)
    Instead, register methods with each socket
    Do not allow hierarchical binding
  Not obliged to register both b_transport and nb_transport
    Automatic conversion (assumes base protocol)
      Variant with no conversion – passthrough_target_socket

## Slide 56: Simple Socket Example
<number>
struct Interconnect : sc_module
{
tlm_utils::simple_target_socket<Interconnect> targ_socket;
tlm_utils::simple_initiator_socket<Interconnect> init_socket;
SC_CTOR(Interconnect) : targ_socket("targ_socket"), init_socket("init_socket")
{
targ_socket.register_nb_transport_fw( this, &Interconnect::nb_transport_fw);
targ_socket.register_b_transport( this, &Interconnect::b_transport);
targ_socket.register_get_direct_mem_ptr(this, &Interconnect::get_direct_mem_ptr);
targ_socket.register_transport_dbg( this, &Interconnect::transport_dbg);
init_socket.register_nb_transport_bw( this, &Interconnect::nb_transport_bw);
init_socket.register_invalidate_direct_mem_ptr(
this, &Interconnect::invalidate_direct_mem_ptr);
}
virtual void b_transport( ... );
virtual tlm::tlm_sync_enum nb_transport_fw( ... );
virtual bool get_direct_mem_ptr( ... );
virtual unsigned int transport_dbg( ... );
virtual tlm::tlm_sync_enum nb_transport_bw( ... );
virtual void invalidate_direct_mem_ptr( ...);
};

## Slide 57: Tagged Simple Sockets
<number>
Target
Interconnect
Initiator
Initiator
Target
simple_target_socket_tagged
simple_initiator_socket_tagged
1
2
1
2
b_transport( id, trans, delay);
Distinguish origin of incoming transactions using socket id

## Slide 58: Tagged Simple Socket Example
<number>
#include "tlm_utils/simple_initiator_socket.h"
#include "tlm_utils/simple_target_socket.h"
template<unsigned int N_INITIATORS, unsigned int N_TARGETS>
struct Bus: sc_module
{
tlm_utils::simple_target_socket_tagged<Bus>* targ_socket [N_INITIATORS];
tlm_utils::simple_initiator_socket_tagged<Bus>* init_socket [N_TARGETS];
SC_CTOR(Bus) {
for (unsigned int id = 0; i < N_INITIATORS; i++) {
targ_socket[id] = new tlm_utils::simple_target_socket_tagged<Bus>(txt);
targ_socket[id]->register_b_transport this, &Bus::b_transport, id );
...
virtual void b_transport( int id, tlm::tlm_generic_payload& trans, sc_time& delay );
...
};

## Slide 59: Many-to-many Binding
<number>
Initiator
Target
tlm_initiator_socket
tlm_target _socket
Initiator
Target
init_socket[0]->b_transport(...)
init_socket[1]->b_transport(...)
target_socket[0]->nb_transport_bw(...)
target_socket[1]->nb_transport_bw(...)
Multi-ports – can bind many-to-many, but incoming calls are anonymous

## Slide 60: Multi-port Convenience Sockets
<number>
multi_passthrough_initiator_socket
multi_passthrough_target_socket
Many-to-many socket bindings
Method calls tagged with multi-port index value

## Slide 61: Socket Summary
<number>
class | Register callbacks? | Multi-ports? | b <-> nb conversion? | Tagged?
tlm_initiator_socket | no | yes | - | no
tlm_target_socket | no | yes | no | no
simple_initiator_socket | yes | no | - | no
simple_initiator_socket_tagged | yes | no | - | yes
simple_target_socket | yes | no | yes | no
simple_target_socket_tagged | yes | no | yes | yes
passthrough_target_socket | yes | no | no | no
passthrough_target_socket_tagged | yes | no | no | yes
multi_passthrough_initiator_socket | yes | yes | - | yes
multi_passthrough_target_socket | yes | yes | no | yes

## Slide 62: THE GENERIC PAYLOAD
Attributes
Memory management
Response status
Endianness
Extensions
<number>

## Slide 63: The Generic Payload
Typical attributes of memory-mapped busses
  command, address, data, byte enables, single word transfers, burst transfers, streaming, response status
Off-the-shelf general purpose payload
  for abstract bus modeling
  ignorable extensions allow full interoperability
Used to model specific bus protocols
  mandatory static extensions
  compile-time type checking to avoid incompatibility
  low implementation cost when bridging protocols
<number>
Specific protocols can use the same generic payload machinery

## Slide 64: Generic Payload Attributes
Attribute | Type | Modifiable?
Command | tlm_command | No
Address | uint64 | Interconnect only
Data pointer | unsigned char* | No (array – yes)
Data length | unsigned int | No
Byte enable pointer | unsigned char* | No (array – yes)
Byte enable length | unsigned int | No
Streaming width | unsigned int | No
DMI hint | bool | Yes
Response status | tlm_response_status | Target only
Extensions | (tlm_extension_base*)[ ] | Yes
<number>
Try DMI !
Array owned by initiator
Array owned by initiator
Consider memory management

## Slide 65: class tlm_generic_payload
<number>
class tlm_generic_payload {
public:
// Constructors, memory management
tlm_generic_payload () ;
tlm_generic_payload(tlm_mm_interface& mm) ;
virtual ~tlm_generic_payload ();
void reset();
void set_mm(tlm_mm_interface* mm);
bool has_mm();
void acquire();
void release();
int get_ref_count();
void deep_copy_into(tlm_generic_payload& other) const;
...
};
Frees all extensions
Construct & set mm
Not a template
Incr reference count
Decr reference count, 0 => free trans
Frees mm’d extensions
mm is optional

## Slide 66: Memory Management Rules
<number>
b_transport – memory managed by initiator, or reference counting (set_mm)
nb_transport – reference counting only
  Reference counting requires heap allocation
  Transaction automatically freed when reference count == 0
  free() can be overridden in memory manager for transactions
  free() can be overridden for extensions
When b_transport calls nb_transport, must add reference counting
  Can only return when reference count == 0
b_transport can check for reference counting, or assume it could be present

## Slide 67: Command, Address and Data
<number>
enum tlm_command {
TLM_READ_COMMAND,
TLM_WRITE_COMMAND,
TLM_IGNORE_COMMAND
};
tlm_command get_command() const ;
void set_command( const tlm_command command ) ;
sc_dt::uint64 get_address() const;
void set_address( const sc_dt::uint64 address );
unsigned char* get_data_ptr() const;
void set_data_ptr( unsigned char* data );
unsigned int get_data_length() const;
void set_data_length( const unsigned int length );
Copy from target to data array
Copy from data array to target
Neither, but may use extensions
Data array owned by initiator
Number of bytes in data array

## Slide 68: Response Status
enum tlm_response_status | Meaning
TLM_OK_RESPONSE | Successful
TLM_INCOMPLETE_RESPONSE | Transaction not delivered to target. (Default)
TLM_ADDRESS_ERROR_RESPONSE | Unable to act on address
TLM_COMMAND_ERROR_RESPONSE | Unable to execute command
TLM_BURST_ERROR_RESPONSE | Unable to act on data length or streaming width
TLM_BYTE_ENABLE_ERROR_RESPONSE | Unable to act on byte enable
TLM_GENERIC_ERROR_RESPONSE | Any other error
<number>

## Slide 69: The Standard Error Response
A target shall either
  Execute the command and set TLM_OK_RESPONSE
  Set the response status attribute to an error response
  Call the SystemC report handler and set TLM_OK_RESPONSE
Many corner cases
  e.g. a target that ignores the data when executing a write – OK
  e.g. a simulation monitor that logs out-of-range addresses – OK
  e.g. a target that cannot support byte enables - ERROR
<number>

## Slide 70: Generic Payload Example 1
<number>
void thread_process() { // The initiator
tlm::tlm_generic_payload trans;
sc_time delay = SC_ZERO_TIME;
trans.set_command( tlm::TLM_WRITE_COMMAND );
trans.set_data_length( 4 );
trans.set_byte_enable_ptr( 0 );
trans.set_streaming_width( 4 );
for ( int i = 0; i < RUN_LENGTH; i += 4 ) { int word = i;
trans.set_address( i );
trans.set_data_ptr( (unsigned char*)( &word ) );
trans.set_response_status( tlm::TLM_INCOMPLETE_RESPONSE );
init_socket->b_transport( trans, delay );
if ( trans.get_response_status() <= 0 )
SC_REPORT_ERROR("TLM2", trans.get_response_string().c_str());
...
}
Would usually pool transactions

## Slide 71: Generic Payload Example 2
<number>
virtual void b_transport( // The target
tlm::tlm_generic_payload& trans, sc_core::sc_time& t) {
tlm::tlm_command cmd = trans.get_command();
sc_dt::uint64 adr = trans.get_address();
unsigned char* ptr = trans.get_data_ptr();
unsigned int len = trans.get_data_length();
unsigned char* byt = trans.get_byte_enable_ptr();
unsigned int wid = trans.get_streaming_width();
if (adr+len > m_length) {
trans.set_response_status( tlm::TLM_ADDRESS_ERROR_RESPONSE );
return;
}
if (byt) {
trans.set_response_status( tlm::TLM_BYTE_ENABLE_ERROR_RESPONSE );
return;
}
if (wid != 0 && wid < len) {
trans.set_response_status( tlm::TLM_BURST_ERROR_RESPONSE );
return;
}
Check for storage overflow
Unable to support byte enable
Unable to support streaming

## Slide 72: Generic Payload Example 3
<number>
virtual void b_transport( // The target
tlm::tlm_generic_payload& trans, sc_core::sc_time& t) {
...
...
if ( cmd == tlm::TLM_WRITE_COMMAND )
memcpy( &m_storage[adr], ptr, len );
else if ( cmd == tlm::TLM_READ_COMMAND )
memcpy( ptr, &m_storage[adr], len );
trans.set_response_status( tlm::TLM_OK_RESPONSE );
}
Execute command
Successful completion

## Slide 73: Byte Enables and Streaming
<number>
unsigned char*
data
unsigned char*
byte_enable
data length = 8
byte enable length = 4
uint64
address
streaming width = 8
streaming width = 4
0xF10
0xF14
0xF10
0xF10
unsigned int
index
0
1
2
3
4
5
6
7
BUSWIDTH/8
LSB
...
...
MSB
LSB
...
...
MSB
0xff
0
0xff
0
1-enable-per-byte
Byte enables applied repeatedly
Data interpreted using BUSWIDTH
Streaming width > 0 => wrap address
#define TLM_BYTE_DISABLED 0x0
#define TLM_BYTE_ENABLED 0xff

## Slide 74: Byte Enable Example 1
<number>
// The initiator
void thread_process() {
tlm::tlm_generic_payload trans;
sc_time delay;
static word_t byte_enable_mask = 0x0000fffful;
trans.set_byte_enable_ptr(
reinterpret_cast<unsigned char*>( &byte_enable_mask ) );
trans.set_byte_enable_length( 4 );
trans.set_command( tlm::TLM_WRITE_COMMAND );
trans.set_data_length( 4 );
...
for (int i = 0; i < RUN_LENGTH; i += 4) {
trans.set_address( i );
trans.set_data_ptr( (unsigned char*)(&word) );
init_socket->b_transport(trans, delay);
...
Uses host-endianness MSB..LSB

## Slide 75: Byte Enable Example 2
<number>
virtual void b_transport( tlm::tlm_generic_payload& trans, sc_core::sc_time& t) // The target
{ ...
unsigned char* byt = trans.get_byte_enable_ptr();
unsigned int bel = trans.get_byte_enable_length();
...
if (cmd == tlm::TLM_WRITE_COMMAND) {
if (byt) {
for (unsigned int i = 0; i < len; i++)
if ( byt[ i % bel ] == TLM_BYTE_ENABLED)
m_storage[adr+i] = ptr[i];
} else
memcpy(&m_storage[adr], ptr, len);
} else if (cmd == tlm::TLM_READ_COMMAND) {
if (byt) {
trans.set_response_status( tlm::TLM_BYTE_ENABLE_ERROR_RESPONSE );
return tlm::TLM_COMPLETED;
} else
memcpy(ptr, &m_storage[adr], len);
}
Byte enable applied repeatedly
byt[i] corresponds to ptr[i]
No byte enables
Target does not support read with byte enables

## Slide 76: Endianness
<number>
Common transfers can use memcpy, width conversions don't modify transaction
Designed to maximize simulation speed
Words in data array are host-endian
Effective word length W = (BUSWIDTH + 7) / 8
Initiators and targets connected LSB-to-LSB, MSB-to-MSB
Most efficient when everything is modeled host-endian
Width-conversions with same endianness as host are free

## Slide 77: Little-endian host
LE Initiator
BE Initiator
LE Target
Neutral Target
BE Target
LE generic payload
data[W-1]
MSB
data[0]
data[0]
data[W-1]
data[W-1]
data[0]
data[0]
data[W-1]
A+W-1
A+0
A+W-1
A+0
A+W-1
A+0
A+W-1
A+0
data[W-1]
data[0]
LSB
MSB
LSB
MSB
LSB
MSB
LSB
mem[W-1]
mem[0]
<number>
Notes: <number>

## Slide 78: Big-endian host
LE Initiator
BE Initiator
LE Target
Neutral Target
BE Target
BE generic payload
data[0]
MSB
data[W-1]
data[W-1]
data[0]
data[0]
data[W-1]
data[W-1]
data[0]
A+W-1
A+0
A+W-1
A+0
A+W-1
A+0
A+W-1
A+0
data[0]
data[W-1]
LSB
MSB
LSB
MSB
LSB
MSB
LSB
mem[W-1]
mem[0]
<number>
Notes: <number>

## Slide 79: Part-word Transfers
Little-endian host
W = 4
length = 6
address = A
data =
A
A+4
1
2
3
4
5
6
Big-endian host
W = 4
length = 6
address = A
data =
A
A+4
4
3
2
1
6
5
byte enable =
0xff
0xff
0xff
0xff
0
0
0xff
0xff
<number>

## Slide 80: Generic Payload Extension Methods
Generic payload has an array-of-pointers to extensions
One pointer per extension type
Every transaction can potentially carry every extension type
Flexible mechanism
<number>
template <typename T> T* set_extension ( T* ext );
template <typename T> T* set_auto_extension ( T* ext );
template <typename T> T* get_extension() const;
template <typename T> void clear_extension ();
template <typename T> void release_extension ();
Freed by ref counting
Sticky extn
Clears pointer, not extn object
mm => convert to auto
no mm => free extn object

## Slide 81: Extension Example
<number>
struct my_extension : tlm_extension<my_extension>
{
my_extension() : id(0) {}
tlm_extension_base* clone() const { ... }
virtual void copy_from(tlm_extension_base const &ext) { ... }
int id;
};
...
tlm_generic_payload* trans = new tlm_generic_payload( mem_mgr );
trans->acquire();
my_extension* ext = new my_extension;
ext->id = 1;
trans.set_extension( ext );
socket->nb_transport_fw( *trans, phase, delay );
trans.release_extension<my_extension>();
trans->release();
Heap allocation
Pure virtual methods
Freed when ref count = 0
User-defined extension
Reference counting
Trans and extn freed

## Slide 82: Extension Rules
<number>
Extensions should only be used downstream of the setter
Whoever sets the extension should clear the extension
If not reference counting, use set_extension / clear_extension
If reference counting, use set_auto_extension
For sticky extensions, use set_extension
Within b_transport, either check or use set_extension / release_extension
Interconnect
Target
Interconnect
Initiator
set
clear
set
clear

## Slide 83: Instance-Specific Extensions
<number>
struct my_extn: tlm_utils::instance_specific_extension<my_extn> {
int num;
};
class Interconnect : sc_module {
tlm_utils::instance_specific_extension_accessor accessor;
virtual tlm::tlm_sync_enum nb_transport_fw( ... )
{
my_extn* extn;
accessor(trans).get_extension(extn);
if (extn) {
cout << extn->num << endl;
accessor(trans).clear_extension(extn);
} else {
extn = new my_extn;
extn->num = count++;
accessor(trans).set_extension(extn);
....
#include "tlm_utils/instance_specific_extensions.h"
Gives unique extensions per module instance

## Slide 84: THE BASE PROTOCOL
tlm_phase
Base protocol rules
Base protocol phases
Defining new protocol types
<number>

## Slide 85: Base Protocol - Coding Styles
Loosely-timed is typically
  Blocking transport interface, forward and return path
  2 timing points
  Temporal decoupling and the quantum keeper
  Direct memory interface
Approximately-timed is typically
  Non-blocking transport interface, forward and backward paths
  4 phases
  Payload event queues
Loosely-timed and approximately-timed are only coding styles
The base protocol defines rules for phases and call order
<number>

## Slide 86: Base Protocol and tlm_phase
<number>
enum tlm_phase_enum { UNINITIALIZED_PHASE = 0,
BEGIN_REQ=1, END_REQ, BEGIN_RESP, END_RESP };
class tlm_phase {
public:
tlm_phase();
tlm_phase( unsigned int id );
tlm_phase( const tlm_phase_enum& standard );
tlm_phase& operator= ( const tlm_phase_enum& standard );
operator unsigned int() const;
};
#define DECLARE_EXTENDED_PHASE(name_arg) \
class tlm_phase_##name_arg : public tlm::tlm_phase { \
...
The base protocol = tlm_generic_payload + tlm_phase
tlm_phase has 4 phases, but can be extended to add new phases

## Slide 87: Base Protocol Rules 1
Base protocol phases
  BEGIN_REQ  END_REQ  BEGIN_RESP  END_RESP
  Must occur in non-decreasing simulation time order
  Only permitted one outstanding request or response per socket
  Phase must change with each call (other than ignorable phases)
  May complete early
Generic payload memory management rules
Extensions must be ignorable
Target is obliged to handle mixed b_transport / nb_transport
Write response must come from target
<number>

## Slide 88: Base Protocol Rules 2
<number>
Timing annotation on successive calls to nb_transport
  for a given transaction, must be non-decreasing
  for different transactions, mutual order is unconstrained
Timing annotation on successive calls to b_transport
  order is unconstrained (loosely-timed)
b_transport does not interact with phases
b_transport is re-entrant
For a given transaction, b_transport / nb_transport must not overlap

## Slide 89: Approximately-timed Timing Parameters
<number>
Initiator
Target
BEGIN_REQ
BEGIN_REQ must wait for previous END_REQ, BEGIN_RESP for END_RESP
END_RESP
Response accept delay
END_REQ
Request accept delay
BEGIN_RESP
Latency of target

## Slide 90: Pre-emption and Early Completion
Permitted phase transition sequences
  BEGIN_REQ
  BEGIN_REQ  END_REQ
  BEGIN_REQ ( END_REQ )  BEGIN_RESP
  BEGIN_REQ  END_REQ  BEGIN_RESP
  BEGIN_REQ ( END_REQ )  BEGIN_RESP  END_RESP
  BEGIN_REQ  END_REQ  BEGIN_RESP  END_RESP
Initiator sends BEGIN_REQ and END_RESP
Target sends END_REQ and BEGIN_RESP
<number>
Transaction completes early if nb_transport returns TLM_COMPLETED

## Slide 91: Examples of Early Completion
<number>
Initiator
Target
Phase
BEGIN_REQ
-, BEGIN_REQ, 0ns
Call
TLM_COMPLETED, -, -
Return
BEGIN_REQ
-, BEGIN_REQ, 0ns
Call
TLM_ACCEPTED, -, -
Return
TLM_COMPLETED, -, -
Return
-, BEGIN_RESP, 0ns
BEGIN_RESP
Call

## Slide 92: Transaction Types
Only three recommended alternatives
  Use the base protocol directly (with ignorable extensions)
  Define a new protocol type class with a typedef for tlm_generic_payload
  Define a new transaction type unrelated to the generic payload
<number>
Do whatever you like with extensions
Sacrifice interoperability; you are on your own
Excellent interoperability

## Slide 93: Protocol Types Class
<number>
struct tlm_base_protocol_types
{
typedef tlm_generic_payload tlm_payload_type;
typedef tlm_phase tlm_phase_type;
};
template <typename TYPES = tlm_base_protocol_types>
class tlm_fw_transport_if
: public virtual tlm_fw_nonblocking_transport_if< typename TYPES::tlm_payload_type,
typename TYPES::tlm_phase_type>
, public virtual tlm_blocking_transport_if< typename TYPES::tlm_payload_type>
, public virtual tlm_fw_direct_mem_if< typename TYPES::tlm_payload_type>
, public virtual tlm_transport_dbg_if< typename TYPES::tlm_payload_type>
{};
template <typename TYPES = tlm_base_protocol_types>
class tlm_bw_transport_if
...

## Slide 94: Defining a New Protocol Types Class
<number>
tlm_initiator_socket<> socket1;
struct my_protocol_types
{
typedef tlm_generic_payload tlm_payload_type;
typedef tlm_phase tlm_phase_type;
};
tlm_initiator_socket< 32, my_protocol_types > socket2;
struct custom_protocol_types
{
typedef my_payload tlm_payload_type;
typedef my_phase tlm_phase_type;
};
tlm_initiator_socket< 32, custom_protocol_types > socket3;
1. Use tlm_base_protocol_types
2. Use new protocol based on generic payload
3. Use new protocol unrelated to generic payload

## Slide 95: Extended Protocol Example 1
<number>
// User-defined extension class
struct Incr_cmd_extension: tlm::tlm_extension<Incr_cmd_extension>
{
virtual tlm_extension_base* clone() const {
Incr_cmd_extension* t = new Incr_cmd_extension;
t->incr_cmd = this->incr_cmd;
return t;
}
virtual void copy_from( tlm_extension_base const & from ) {
incr_cmd = static_cast<Incr_cmd_extension const &>(from).incr_cmd;
}
Incr_cmd_extension() : incr_cmd(false) {}
bool incr_cmd;
};
struct incr_payload_types
{
typedef tlm::tlm_generic_payload tlm_payload_type;
typedef tlm::tlm_phase tlm_phase_type;
};
User-defined protocol types class using the generic payload

## Slide 96: Extended Protocol Example 2
<number>
struct Initiator: sc_module
{
tlm_utils::simple_initiator_socket< Initiator, 32, incr_payload_types > init_socket;
...
void thread_process()
{
tlm::tlm_generic_payload trans;
...
Incr_cmd_extension* incr_cmd_extension = new Incr_cmd_extension;
trans.set_extension( incr_cmd_extension );
...
trans.set_command( tlm::TLM_WRITE_COMMAND );
init_socket->b_transport( trans, delay );
...
trans.set_command( tlm::TLM_IGNORE_COMMAND );
incr_cmd_extension->incr_cmd = true;
init_socket->b_transport( trans, delay );

## Slide 97: Extended Protocol Example 3
<number>
// The target
lm_utils::simple_target_socket< Memory, 32, incr_payload_types > targ_socket;
virtual void b_transport( tlm::tlm_generic_payload& t rans, sc_core::sc_time& t )
{
tlm::tlm_command cmd = trans.get_command();
...
Incr_cmd_extension* incr_cmd_extension;
trans.get_extension( incr_cmd_extension );
if ( incr_cmd_extension->incr_cmd ) {
if ( cmd != tlm::TLM_IGNORE_COMMAND ) {
trans.set_response_status( tlm::TLM_GENERIC_ERROR_RESPONSE );
return;
}
++ m_storage[adr];
}
...
Assume the extension exists
Detect clash with read or write

## Slide 98: ANALYSIS PORTS
Analysis Interface and Ports
<number>

## Slide 99: Analysis Ports
Module n
<number>
Module m
Analysis port p
Analysis port q
Subscriber s1
struct Subscriber: sc_object, tlm::tlm_analysis_if<int>
{
Subscriber(char* n) : sc_object(n) {}
virtual void write(const int& t) { ... }
};
tlm::tlm_analysis_port<int> p;
m.p.bind( q );
n.q.bind(s1);
n.q.bind(s2);
n.q.bind(s3);
Subscriber s2
Subscriber s3
Analysis port may be bound to 0, 1 or more subscribers
p.write(99);

## Slide 100: Analysis Interface
<number>
template <typename T>
class tlm_write_if : public virtual sc_core::sc_interface {
public:
virtual void write(const T& t) = 0;
};
template < typename T >
class tlm_analysis_if : public virtual tlm_write_if<T> {};
class tlm_analysis_port : public sc_core::sc_object , public virtual tlm_analysis_if< T > {
public:
void bind( tlm_analysis_if<T> &_if );
void operator() ( tlm_analysis_if<T> &_if );
bool unbind( tlm_analysis_if<T> &_if );
void write( const T &t ) {
for( i = m_interfaces.begin(); i != m_interfaces.end(); i++ ) {
(*i)->write( t );
}
}
};
write() sends transaction to every subscriber
"Non-negotiated"

## Slide 101: Analysis Port Example
<number>
struct Subscriber : sc_object, tlm::tlm_analysis_if<Trans> {
Subscriber ( const char* n ) : sc_object(n) { }
virtual void write( const Trans& t ) {
cout << "Hello, got " << t.i << "\n";
}
};
SC_MODULE (M) {
tlm::tlm_analysis_port<Trans> ap;
SC_CTOR (M) : ap("ap") {
SC_THREAD (T);
}
void T () {
Trans t = { 999 };
ap.write( t );
}
};
SC_MODULE (Top) {
M* m;
Subscriber* subscriber1;
Subscriber* subscriber2;
SC_CTOR(Top) {
m = new M("m");
subscriber1 = new Subscriber("subscriber1");
subscriber2 = new Subscriber("subscriber2");
m->ap.bind( *subscriber1 );
m->ap.bind( *subscriber2 );
}
};
Subscriber implements analysis interface, analysis port bound to subscriber

## Slide 102: Summary: Key Features of TLM-2
<number>
Transport interfaces with timing annotation and phases
DMI and debug interfaces
Loosely-timed coding style and temporal decoupling for simulation speed
Approximately-timed coding style for timing accuracy
Sockets for convenience and strong connection checking
Generic payload for memory-mapped bus modeling
Base protocol for interoperability between TL- models
Extensions for flexibility of modeling

## Slide 103: For further information visit www.systemc.org